## Slide 1: FallingTalk: An IoT-Based Real-Time Falling Detection System
2021/01/19 ver2.2
Speaker: 林明佑, 黃胤錚
Advanced Design and Implementation of IOT Applications

## Slide 2: Outline
Abstract
Motivation
Introduction
Results
Discussion

## Slide 3: Abstract
We present a system for detection of human falling from web-cam or video for support of elderly people living alone in their homes.
In this system, we have the main two parts, which are IoTTalk part and Detection part.
IoTTalk part, including DAI and Line API.
Detection part, including MHI Calculator and Falling Detector.
The algorithms in this system are implemented in C++, Python with OpenCV and ZeroMQ library.

## Slide 4: Overview
Overview of FallingTalk
Input Image
Motion History Image
Background Subtraction
Shape analysis
MHI coefficient calc()
Image-Based solution
Feature vector contains
(width of human)
(height of human)
Cmotion(MHI coefficient)
(shape change parameter)

## Slide 5: Overview
IoT-Based solution(IoTtalk)
FallingTalk_Server
IoTtalk Server
Line API
Warning Message

## Slide 6: Outline
Abstract
Motivation
Introduction
Results
Discussion

## Slide 7: Motivation
隨著近年來社會高齡化的趨勢，我們會需要一些方法來幫助老年人來提高其獨居的能力[1]
在此Project，我們希望能夠提出一個方法，透過IoTTalk來及時通報老年人有無跌倒現象的發生
[1]鍾文平教授「智慧醫療」演講
Notes: 1993進入高齡化社會
2018進入高齡社會
預估2074年將進入超高齡社會

## Slide 8: Outline
Abstract
Motivation
Introduction
Results
Discussion

## Slide 9: PeopleDetector(optional)
使用HOG Feature + SVM來進行判斷畫面內是否是“人”
Linear SVM
Ref :https://www.researchgate.net/figure/Calculation-steps-of-the-HOG-descriptor_fig1_261285146
Result

## Slide 10: FallDownDetector
使用BackgroundSubstractor(Gaussian Mixture-Based)來繪製運動輪廓
並透過IOU Checker來對每個進入畫面的人進行Label
新影像
BackgroundSubstractor
IOU Checker
Shape analysis
Result
計算MHI Coefficient
Server

## Slide 11: FallingTalk Server, FallingTalk Line
Server負責接收當前是否有跌倒狀況發生並push data到IoTTalk
Line 負責從IoTtalk server pull data 並傳送訊息到Line

## Slide 12: Outline
Abstract
Motivation
Introduction
Results
Discussion

## Slide 13: Experiment Setup
OpenCV 4.2.0
Python 3.7.0
C++ 11(or later)
ZeroMQ
1920 x 1080p resolution web-camera

## Slide 14: Dataset
Video Recording in NCTU EC015
Fall detection Dataset
Fall detection Dataset | 108 selected frames
Video Recording in EC015 | 94 selected frames

## Slide 15: Motion History Image(MHI)
Walk
Sit
Fall

## Slide 16: BackgroundSubstractor + Shape Analysis + MHI
Walk
Stand

## Slide 17: BackgroundSubstractor + Shape Analysis + MHI
Fall
Fall

## Slide 18: Recognition Results Summary
Recognition results summary
91.1% accuracy
Action | Test Positive(Detected) | Test negative(Not Detected)
Fall | 91 | 2
normal | 16 | 93

## Slide 19: IoTtalk + Line API

## Slide 20: Outline
Abstract
Motivation
Introduction
Results
Discussion

## Slide 21: Discussion
We implement an IoT-based real-time falling detection system with high accuracy.
FallingTalk can track a person and LINE users in real-time with message and picture
In the future，我們希望能夠為FallingTalk加上聲音感測器、三軸加速度感測器、陀螺儀、心率等等，增加多個features，以最佳化偵測老年人的健康狀態完成一套完整健康偵測系統。